## Slide 1: Use of OpenFOAM coupled with a Hybridization of Finite Element-Boundary Element Methods using an Adaptive Absorbing Boundary Condition for Wind Noise Simulation
N. ZERBIB
ESI GROUP, VA CoE, 8 rue Clément Bayard, 60200 Compiegne, France, nicolas.zerbib@esi-group.com
Conference in Honor of
Professor Abderrahmane Bendali
PAU, December 12-14 2017

## Slide 2: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Scenario:
  Turbulent flow around structure (mirror/A-pillar for automotive)
  Pressure loadings on the structure (windows as elastic surfaces), the rest is considered rigid
  Transmission through the windows to the interior of the vehicule by vibration (interior noise) or pass-by noise contribution (other applications: pantograph for train, landing gear for aircraft)

## Slide 3: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Specification and Objectives:
  Efficient and Robust numerical methods to predict the noise generation phenomena and propagation around very complex and large structures on a very large frequency domain
  Optimize the CPU time of these methods to be able to realize some parametric studies during the conception phase
Hypothesis:
  Low Mach number ()
  High Reynolds number ()
Challenges:
  Pressure field includes convective and acoustic components
  Acoustic component ~30-70 dB smaller in amplitude than convective one
  Acoustic component highly directional
  Both components contribute to SPL at driver‘s ear

## Slide 4: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Specification and Objectives:
  Efficient and Robust numerical methods to predict the noise generation phenomena and propagation around very complex and large structures on a very large frequency domain
  Optimize the CPU time of these methods to be able to realize some parametric studies during the conception phase
Hypothesis:
  Low Mach number ()
  High Reynolds number ()
Aero-Acoustic Analogies: weak coupling between 2 phenomena
  A first CFD computation to determine the equivalent aero-acoustic sources
  A second acoustic simulation to model the propagation of those previous sources (in the medium at rest for this presentation).

## Slide 5: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Methodology:
Efficient and Robust
Optimize the CPU time
Aero-Acoustic Analogies

## Slide 6: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Methodology:
Efficient and Robust
Optimize the CPU time
Aero-Acoustic Analogies

## Slide 7: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Test Case: SAE Body
  Ref: “Wind Noise caused by the A-pillar and the Side Mirror flow of a Generic Vehicle Model”, AIAA2012, M. Hartmann, J. Ocker,T. Lemke, A. Mutzke, V. Schwarz, H. Tokuno, R. Toppinga, P. Unterlechner, G. Wickern
  The SAE body is a generic automotive geometry structure built out of stiff foam
  It allows competing automotive manufacturers to study physical phenomena without disclosing any confidential information related to a particular vehicle design
  An automotive type side glass fitted into the SAE body wall
  It reflects similar geometry conditions as in real vehicle, with the presence of a slope in the front (windshield), presence of A-Pillar and side mirror.

## Slide 8: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Interior Vibro-Acoustic validation: reciprocity principle
5 microphones are located inside SAE body to monitor interior sound field
An omnisource is located inside the SAE body to fill interior volume with a strong acoustic field

## Slide 9: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Exterior Vibro-Acoustic validation: reciprocity principle
v

## Slide 10: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Methodology:
Efficient and Robust
Optimize the CPU time
Aero-Acoustic Analogies

## Slide 11: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
CFD computation: incompressible DDES delivers the aerodynamic pressure (OpenFoam)
Conservative mapping from the source mesh (CFD) to the target mesh (acoustic). Use specific/adapted mesh for each physics. Fast Fourier Transform Time to Frequency domain
Acoustic propagation using analogies by Boundary Element, Finite Element Methods or FEM/BEM hybridization (VAOne)
Process of CAA for Flow induced noise:

## Slide 12: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Volume source term
Acoustic pressure
Surface source term, aerodynamic pressure from incompressible CFD
Curle analogy [1,2,3,4]:
static solution ()
Incompressible flow at low Mach number
Lighthill Tensor (high Reynolds number):

## Slide 13: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Citations to the Curle’s work
Total number of citations to the 1955 paper: 482

## Slide 14: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Lighthill analogy [5,6,7]:
/
CFD Sources
Sources : vectorField from the CFD
Volume sources
at low cost

## Slide 15: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Lighthill analogy [5,6,7]:
Sources : scalarField from the CFD
/
CFD Sources
Volume sources
at low cost

## Slide 16: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Citations to the M.J. Lighthill ‘s work
Total number of citations to the 1952 paper: 1787

## Slide 17: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Results for Simple Ducted Diaphragm
Results : SPL on a sensor downstream on the surface for [200:20:3500] Hz
BEM (Mesh: Nodes, T3: , DMP16) : 1’05’’ / segment
FEM (Mesh: Nodes, TE4: , Nodes, T3: ), DMP16: 0’09’’ / segment, Nodal (Direct Solve), DMP16: 0’03’’ / segment Modal (InDirect Solve)
Inlet/Outlet boundaries are set to non-reflective conditions

## Slide 18: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Results for Simple Ducted Diaphragm
X = 0 m
Y = 0,0387 m
Z = 1,285 m
A
SPL at point A – Comparison between experimental measurements and both aero-acoutic analogies

## Slide 19: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
BEM Curle | FEM Lighthill
Only Surface Mesh (easy task) | 3D Volume Mesh (can be difficult)
Small Number of DoF | Large Number of DoF
Adapted for Interior and Exterior domain | Adpated for Interior Domain but not really for Exterior problem (PML)
Symmetric Dense Complex Matrices (RAM: O(N2) and CPU: O(N3)) | Symmetric Sparse Complex Matrices (RAM: O(N) and CPU: O(N2))
Equivalent Aero-acoustic Sources on the Surface (Dipoles) and in the Volume (Quadrupoles but not adapted for BEM) | Full 3D volume description of the Equivalent Aero-acoustic Sources
Direct Method | Direct (Nodal) and Indirect (Modal for cavity) Method

## Slide 20: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Acoustic pressure
Volume source term, aerodynamic pressure from incompressible CFD
Hybrid Lighthill analogy [8,9,10,11]:

## Slide 21: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
/
Acoustic pressure
Volume source term, aerodynamic pressure from incompressible CFD
Hybrid Lighthill analogy [8,9,10,11]:

## Slide 22: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
/
Volume FEM operators in
CFD Sources
Hybrid Lighthill analogy [8,9,10,11]:

## Slide 23: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Surface integral
operators (AABC)
between S and
Hybrid Lighthill analogy [8,9,10,11]:
/

## Slide 24: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Volume Surface integral operators (for sources)
/
CFD Sources
Hybrid Lighthill analogy [8,9,10,11]:

## Slide 25: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
R
Hybrid Lighthill analogy [8,9,10,11]:

## Slide 26: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
1
Consistent or
Inconsistent 3D
Conservatice
Mapping (on-the-fly)
Hybrid Lighthill analogy [8,9,10,11]:

## Slide 27: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Conservative
mapping
.
.
.
.
.
.
.
.
.
.
Unstructured CFD mesh (Source Mesh)
Pressure located at the
center of the cells (107)
Tetra Acoustic mesh (Target Mesh)
Pressure located at the center
of the cells (105) (P0), at the vertices (P1), …
.
.
.
.
.
.
.
.
.
107
105
3D Volume Conservative Interpolation [12]:

## Slide 28: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
3D Volume Conservative Mapping [12]:
  Cell Volume Weight (CVW) Interpolation implemented in OpenFOAM
  Computation of intersecting volumes computationally costly (solved by HPC) but very high quality interpolation
    CVW method conserves the integral over the interpolated quantity exactly.
    Computation of the Interpolation Operator before the time loop and application on the results on-the-fly at the end of the converged time before the export of the quantities (Minimum disk storage).
Cell volume intersections for the CVW method (courtesy [12])

## Slide 29: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Incompessible DES OpenFOAM computation over a Sphere [13]
Parameters of the DDES case (incompressible)
Inlet/Outlet & Boundary Conditions
Dimensions
Turbulence model | Spalart-Allmaras DDES
Time step | 3.10-5 s (record 1/3 steps)
Simulated physical time | 0.7 s (record on the last 0.3 s)
Time calculation | ~20h
Computing resources | 16 CPUs (Sandy Bridge machine Intel Xeon E5-2680 2.7 Ghz)
Inlet condition (Left Patch) | Constant Ux = 33 m/s
Outlet conditions | Standard Wall Function
Mesh | Hexahedral
Base size (level 0) | 0.004 m
Sphere size (level 4) | 0.000025 m = Base size / 24
Number of layer in the BL | 5
Thickness of the BL | 0.25 mm
Thickness of near wall prism layer | 0.1 mm
Total Nomber of cells | 12.9 M
Sphere Radius | 0.25m
Duct Length | 8m
Duct Width and Height | 1m
Xmin Patch | -0.25m

## Slide 30: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Incompessible DES OpenFOAM computation over a Sphere [13]

## Slide 31: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Acoustic computation (CFD Loading, Frequency Range [200:20:3500]Hz)
Surface Mesh (BEM):
  Nodes: 9 140
  Elements: 18 276
AABC layer; Distance D=10cm
  Nodes: 13 692
  Elements: 27 380
Volume Mesh (FEM)
  Nodes: 172 728
  Elements: 958 959
R
D

## Slide 32: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Acoustic computation (CFD Loading, Frequency Range [200:20:3500]Hz)
Surface Mesh (BEM):
  Nodes: 35 406
  Elements: 70 808
AABC layer; Distance D=10cm
  Nodes: 35 406
  Elements: 70 808
Volume Mesh (FEM)
  Nodes: 353 667
  Elements: 1 963 883
R
D

## Slide 33: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Acoustic computation (CFD Loading, Frequency Range [200:20:3500]Hz)
Surface Mesh (BEM):
  Nodes: 9 140
  Elements: 18 276
AABC layer; Distance D=10cm
  Nodes: 13 692
  Elements: 27 380
Volume Mesh (FEM)
  Nodes: 172 728
  Elements: 958 959
Volume Source Mesh (CFD Data)
  Nodes: 471 345
  Elements: 2 875 812

## Slide 34: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Curle BEM vs Lighthill Hybrid-FEM (2.5kHz)
Curle BEM
Lighthill Hybrid-FEM

## Slide 35: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Curle BEM vs Lighthill Hybrid-FEM
Sequential (1 proc) | BEM Curle Coarse/Fine | Lighthill Hybrid-FEM (Coarse/Vol Source) | Lighthill Hybrid-FEM (Fine/Vol Source) | Lighthill Hybrid-FEM (Coarse+Box/Vol Source)
1 Freq CPU TIME (mn) | 5 / 95 | 5 / 2.5 (3iter) | 17 / 10 (3iter) | 13 / 6 (3iter)
Total CPU Time (Hour) | 14 / 10D | 14 | 47 | 35
RAM (Gb) | 0.8 / 13 | 0.3 | 1.6 | 0.5

## Slide 36: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Surface Mesh
  Number of Nodes: 144 649
  Number of Elements: 289 294
AABC surface:
  Number of Nodes: 144 649
  Number of Elements: 289 294
Target Application: SAE Car Body
Volume (FEM):
  Number of Nodes: 391 357
  Number of Elements: 1 477 394
Volume Source:
  Number of Nodes: 708 621
  Number of Elements: 3 564 978

## Slide 37: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Target Application: SAE Car Body
  Acoustic Load
    1 monopole behind the side mirror
Sequential (1 proc) | Standard BEM | MLFMM | Hybrid-FEM
1 Freq CPU TIME (mn) | 4444 (74H) | 134 (2.3H / 45 iter) | 10 (6 iter)
Total CPU Time (Hour) | 3185 (132D) / 12D DMP16 | 397 / 27H DMP16 | 38.5 / 2H DMP16
RAM (Gb) | 170 | 23 | 12 / 192

## Slide 38: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
Conclusions:
  Presentation of an extension of the FEM Lighthill analogy using an Adaptive Absorbant Boundary Condition usefull for external turbulent flow noise applications (Automotive, Train)
    No neglected terms for aeroacoustic sources in the formulation (Source domain definition different from the acoustic computational domain)
    No constraint on shape and distance for the AABC surface (until simple extrusion of original surface, control the acoustic computational domain)
    Use on-the-fly 3D no-consistent conservative mapping (control the disk storage)
    Extension of MLFMM algorithm to compute Surface/Volume integral operators (savings CPU Time and RAM)
  Application on academic case and very first comparison vs Curle BEM analogy
    Coherent results with Curle BEM analogy
    Very significant saving time and RAM requirements (potential factor 150 speed-up for very large model)
Perspectives and Future Work:
  To reduce peaky results:
    Add space filtering during non-consistent mapping (Hann Window)
    Use averaging between several segments of the time domain CFD results
  Study of the « CFD » source mesh (refinement, dimension/shape of the source domain, etc…)
  Validation against experiments
  Demonstrate impact of volume sources (quadrupoles) on specific cases
  Application on more complex industrial case for Wind Noise
  (SAE Body for Automotive, Pantograph for train or Landing Gear for plane)

## Slide 39: Conference in Honor of Professor Abderrahmane Bendali
HYBRID FINITE AND BOUNDARY ELEMENT METHODS FOR AERO-ACOUSTIC APPLICATIONS
References:
  Curle Analogy
    [1] N. Curle, The Influence of Solid Boundaries upon Aerodynamic Sound, Proceedings of the Royal Society A: Mathematical, Physical and Engineering Sciences 231(1187): 505-510, 1955
    [2] M. Watrigant, C. Picard, E. Perrey-Debain and C. Prax, Formulation adaptée de l’analogie acoustique de Lighthill-Curle en Zone Source, Proceedings of the 19th French Congress of Mechanics, Marseille, France, 2009
    [3] C. Schram, A Boundary Element Extension of Curles analogy for Non-Compact Geometries at Low-Mach Numbers, Journal of Sound and Vibration 322(2009): 264-281, 2009
    [4] N. Papaxanthos and E. Perrey-Debain, On the use of integral formulations for the prediction of air flow noise in ducts, Proceedings of the 22th International Congress on Sound and Vibration, Florence, Italy, 2015
  Lighthill Analogy
    [5] M.J., Lighthill, On sound generated aerodynamically. Part I: General theory. Proceedings of the Royal Society of London, 564-587, (1952).
    [6] M., Piellard, C., Bailly, Validation of a hybrid CAA method. Application to the case of a ducted diaphragm at low Mach number; Proceedings of the 14th AIAA/CEAS Aeroacoustics Conference, Vancouver, British Columbia, 2008.
    [7] N., Zerbib, L., Mebarek, A., Heather, M., Escouflaire, Use of OpenFoam coupled with the Finite Element Method for Computational AeroAcoustics , Proceedings of the 4th OpenFOAM User Conference 2016, Cologne – Germany, 2016.
  Adaptive Absorbing Boundary Condition
    [8] S. Alfonzetti, G, Borzi, FEM Solution to High-Frequency Unbounded Problems by means of RBCI, Proceedings International Workshop on Finite Elements for Microwave Engineering, Chios (Greece), May 2002
    [9] N. Zerbib and al , “Méthodes de sous-structuration et de décomposition de domaine pour la résolution des équations de Maxwell. Application au rayonnement d'antenne dans un environnement complexe“, Thesis, INSA Toulouse, 2006.
    [10] A. Bendali and al , “Localized adaptive radiation condition for coupling boundary and finite element methods applied to wave propagation problems“, IMA Journal of Numerical Analysis. 01/2014; 34(3), 2014.
    [11] N. Zerbib and al , “An extension of the adaptive absorbing boundary condition method“, Conference: Antennas and Propagation Society International Symposium, 2007 IEEE.
  Conservative Mapping
    [12] T. Schroder, P. Silkeit, O. Von Estorff, Influence of source term interpolation on hybrid computational aeroacoustics in finite volumes, Proceedings of Internoise 2016, Hamburg, Germany, 2016.
  Validation example of turbulent flow around a sphere (CFD)
    [13] G. Constantinescu, Numerical investigations of flow over around a sphere in the subcritical and supercritical regimes, Physics of fluid, Volume 16, Number 5, May 2004..

## Slide 40
Best Wishes Abderrahmane !